N9803C Aircraft Weight and Balance Worksheet
Baseline data from Weight and Balance Calculated on 9/7/07	Baseline		This Flight
	Weight (lbs)	Moment / (lb-inch/1000)	Weight / (lbs)	Moment / (lb-inch/1000)
Licensed Empty Weight	1453.4	54.5
Engine Oil / (8 quarts, 2 lbs/quart)	15	-0.2
Pilot and Front Seat Passenger	360	13.5
Rear Seat Passengers and Baggage on Rear Seat	40	3.0
Baggage in Rear Area / (10 lbs of supplies typical)	10	1.0
Zero Fuel Weight / Moment	1878.4	71.8
Fuel (Std 48 gal, 6 lbs/gal)	288	13.8
Taxi Weight / Moment	2166.4	85.6
Fuel consumed for Taxi / Runup / (less 0.8 gal, 6 lbs/gal)	-4.8	-0.2
Takeoff Weight	2161.6	85.4