C182 Normal Procedures (1)

BEFORE STARTING
Weight and Balance	COMPLETE
Fuel Quantity and Quality	CHECK
Start Times	RECORDED
Seat and Seat Belts	ADJ / LOCKED
Brakes	TEST
Flight Controls	CHECK (box)
Fuel Selector	BOTH
Flaps	UP
Mixture	CUTOFF
Propeller	HIGH RPM
Throttle	CLOSED
Carburetor Heat	OFF
Avionics	OFF

STARTING
Mixture	RICH
Prime (Cold Start Only)	ONE STROKE
Master Switch	PULL ON
Beacon Strobe	ON
Propeller Area	CLEAR
Throttle	OPEN ½ INCH
Ignition Switch	BOTH
Brakes	HOLD
Starter Button	PUSH
Throttle	800-1000 RPM
Mixture	LEAN for taxi

GROUND CHECK
Mixture	RICH
Throttle	1700 RPM
Propeller	CYCLE ONCE
Magnetos (Max 125 RPM)	CHECK
Carburetor Heat	CHECK
Oil Pressure (30-60 PSI)	CHECK
Ammeter (Charging)	CHECK
Throttle	1000 RPM

BEFORE TAKEOFF
Fuel Selector	BOTH
Trim	SET TAKEOFF
Flaps	SET 10 DEG
Engine Monitor	SCAN
Instruments	SET
Transponder	ALT

NORMAL TAKEOFF
Brakes	HOLD
Throttle	OPEN (slowly)
Brakes	RELEASE
Rotate	60 MPH
Airspeed	80 MPH
Flaps	RETRACT
Airspeed	90 MPH

C182 Normal Procedures (2)

CLIMB
Throttle	FULLY OPEN
Propeller (at 25” MP)	2600 RPM
Mixture (below 23” MP)	LEAN
Airspeed	90->80MPH
Engine Gauges	CHECK
Fuel Selector	BOTH

JUMP RUN
Propeller	2200 RPM
Throttle	13-15” MP
Airspeed	75-80 MPH
Jump Door	OPEN
Carburetor Heat	ON (slowly)

DESCENT
Jump Door	LOCKED
Throttle	18” MP
Engine Monitor	SET CH 6
CHT (1 deg drop / 2 sec)	Monitor
Airspeed	150 MPH
Throttle (Adjust)	18” MP

LANDING
Fuel Selector	BOTH
Flaps	AS REQUIRED
Mixture	RICH
Propeller	HIGH RPM
Carburetor Heat	ON
Airspeed	80 MPH

AFTER LANDING
Flaps	UP
Carburetor Heat	OFF
Transponder	STANDBY

SHUTDOWN
Avionics	OFF
Mixture	CUTOFF
Ignition Switch	OFF
Master Switch	OFF
End Times	RECORDED

General Information / Fuel Per Tank (Gal): 30 max / 27.5 usable / Fuel Consumption: 14 GPH (average) / Per Jump Load to 10K: 0.6 tach / 8 Gal. (ave) / Oil Level (Qt) Min/Nom/Max: 8 / 10 / 12 / Airspeeds (MPH): / Vr: 60, Vy: SL = 89 / 10K = 81, Va: 120 / Nominal Loaded Climb Rates (FPM) / Sea Level = 1200, 10K = 500